## Slide 1: Current Intensity and Voltage

## Slide 2: 5.4 Current Intensity
Symbol: I
Units: Amperes, A
Current: the amount of electrons that flow through a wire
Example: 0.7 amperes is shown by
I = 0.7 A
An ammeter is the instrument used to measure current intensity. It has to be placed where the charge passes!
A
Write this in your notebook.

## Slide 3: Current Intensity
The current intensity in a circuit can be determined using the formula:
I = q
∆t
I is the current intensity in amps (A)
q is the charge in coulombs (C)
t is time in seconds (s)
Write this in your notebook.

## Slide 4: Ex #1
What is the current flowing through a car headlight if there are 900 C of charge used in 1 minute?
I = q
Δt
= 900 C
60 s
I = 15 A
Write this in your notebook.

## Slide 5: Ex #2:
How much charge does it take to operate an MP3 player for 15 minutes if the current is 2A?
I = q
Δt
Write this in your notebook.

## Slide 6: Ex #3:
A car headlight uses 6A. How long would it shine if it received a charge of 900 C?
I = q
Δt
Write this in your notebook.

## Slide 7: 5.5 Potential Difference (Voltage)
Symbol: V
Units: Volts, V
Potential Difference what causes the electrons to flow through the wire. (kind of like “water pressure”)
  Provided by a battery or power supply
Example: V = 12V
A voltmeter is used to measure potential difference
V
Write this in your notebook.

## Slide 8: Potential Difference (Voltage)
The potential difference in a circuit can be determined using the formula:
V=E
q
V is potential difference in volts (V)
E is the energy in joules (J)
q is the electric charge in coulombs (C)
Write this in your notebook.

## Slide 9: Ex #1
In a house, how much energy is provided by 120V service providing 200C of charge?
V=E
q
Write this in your notebook.

## Slide 10: 5.6 Resistance
Symbol: R
Units: Ohms, Ω
Resistance is how difficult it is for current to flow
Resistance is the opposite of conductance!
A resistor is used to slow current down and convert electrical energy into heat energy (e.g. light bulb, stove element).
Write this in your notebook.

## Slide 11: 5.7 Ohm’s Law
This formula shows the relationship between Resistance (R), current intensity (I) and potential difference (V).
V = RI
Write this in your notebook.
# of ohms (Ω)
# of amps (A)

## Slide 12: Summary Table
 | Resistance | Current | Potential Difference
Definition | Ability to slow current down | Is a measurement of the flow of electrons | Pushing the electrons thru the wires
Symbol | R | I | V
Units | Ohms (Ω) | Amps (A) | Volts (V)
Formula (if applicable) | V= RI | I = q ∆t | V = E q
How is it measured (if applicable) | calculated | Ammeter or calculated | Voltmeter or calculated

## Slide 13: Class Work
P172 Textbook
  #1, 2, 3
  #4
  #7, 8
  #10
  #12
  #13, 16

## Slide 14: Stop here

## Slide 15: Colour coding on resistors
Resistors are coated with ceramic.
They have colour coded bands to indicate the resistance strength!

## Slide 16: Resistor
1st colour = 1st #
2nd colour = 2nd #
3rd colour = # of zeros
Black 0
Brown 1
Red 2
Orange 3
Yellow 4
Green 5
Blue 6
Violet 7
Gray 8
White 9
2
1st
2nd
3rd
3
0 000 W